Wiring Diagram M.Y.’86 to ’87 Mirrors

BR

YE

MM

MIRROR								    GR

GN

WT           BL            BR               BR            RE         BK		DO NOT

USE THESE

FOUR WIRES

CAR			     BR

WT                   WT                 BR         GR/GN      BK        BK           YE               GN

NOTE: - TO CHANGE HORIZONTAL TO VERTICAL MOVEMENT, SWAP WT & BL MIRROR WIRES

WITH RE & BK WIRES

- TO SWAP LINEAR MOTION OF A PARTICULAR MOVEMENT, SWAP PAIR OF  WIRES

(EXAMPLE: SWAP WT WITH BL  AND/OR  RE WITH BK)

- DO NOT USE FOUR OTHER WIRES AS THEY SERVE SEAT/MIRROR MEMORY ONLY

- DO NOT REPLACE WINDOW/WINDOW DIRECTION SWITCH

BL-BLUE    		BK-BLACK    	              GR-GREY	      YE-YELLOW

GN-GREEN                        WT-WHITE                        BR-BROWN                RE-RED

GR/GN-GREY WITH GREEN STRIPE

# Text boxes

MOTOR

MOTOR

HEATER